This document explains how to calibrate a droplet for motion and what API funciton calls to use to do it.

The calibration has to be done manually through the terminal

cmd set_motors "direction_number" "value0" "value1" "value2"
This command sets the the direction_number from 0 to 7 and for each direction the three values denote the value of each of the three motors.
For example, "cmd set_motors 0 0 -600 450" sets the value of the motors in direction 0 as 0, anti-clockwise 600 and clockwise 450.
The convention followed for direction_number is 0 is the forward direction, 6 is the clockwise rotation and 7 is anti clockwise direction.
Once this is done, you can verify if you have assigned the values appropriately for that particular dropelt for motion by moving it around.

cmd move_steps "direction" "steps"
This command move the droplet in the particular direction for the mentioned number of steps. This can be used to verify if the motors for motion have been calibrated properly.
If the droplet is way off in its motion, then the dropelts can be recalibrated using step 1 and then tested again.

Once the calibration has been done for all the required directions, their values can be written to the EEPROM using the cmd write_motor_settings command from the terminal. This ensures that the droplet stays calibrated even after a power on reset.